| Technical Specification |
| --- |
| Version | 2.8 CRD SWB | 2.8 CRD Unlimited LWB |
| Fuel System | Common Rail Turbo Diesel |
| Capacity | 2,776cc |
| Max Power | 200hp @ 3,600 RPM |
| Max Torque | 460Nm @ 1,600 RPM Auto / 410Nm @ 2,600 RPM Manual |
| 4WD System | Command-Trac® Part-Time 4X4, 2-Sp Transfer Case |
| Transmission | 6s Man | 5s Auto | 6s Man | 5s Auto |
| Acceleration 0-100km/h | 10.6 secs | 10.6 secs | 11.1 secs | 10.7 secs |
| Top Speed | 172 km/h | 172 km/h | 172 km/h | 172 km/h |
| Economy (Combined Cycle) | 7.1 L/100km | 8.1 L/100km | 7.4 L/100km | 8.3 L/100km |
| CO2 Emissions | 187g/km | 213g/km | 194g/km | 217g/km |
| VRT Band | E/€630p.a. | F/€1,050p.a. | F/€1,050p.a. | F/€1,050p.a. |
| Kerb Weight | 1,975kg | 1,933kg | 2,128kg | 2,073kg |
| Length | 4,223mm | 4,751mm |
| Width (excl. mirrors) | 1,873mm | 1,877mm |
| Overall Height | 1,800 – 1,840mm (depending on wheels) |
| Wheelbase | 2,424mm | 2,947mm |
| Boot Space | 141L – 714L | 498L – 934L |
| Fuel Tank Capacity | 66.6 litres | 85.0 litres |
| Service Intervals | 12 months / 20,000km | 12 months / 20,000km |
| Approach Angle (wheel size) | 37.8º (16, 17, 18) | 37.6º(16) 37.8º(17, 18) |
| Departure Angle (wheel size) | 29.7º(16) 31.3º(17) 31.6º(18) | 29.8º(16) 31.4º(17) 31.7º(18) |
| Breakover Angle | 25.5º (16, 17, 18) | 20.9º (16) 20.0º (17, 18) |
| Ground Clearance 16”Wheels | F:243.8mm R:238.8mm | F:243.8mm R:236.2mm |
| Ground Clearance 17”Wheels | F:266.7mm R:259.1mm | F:266.7mm R:256.5mm |
| Ground Clearance 18”Wheels | F:269.2mm R:261.6mm | F:266.7mm R:259.1mm |
| Wading Depth | 482.6mm |
| Steering | Recirculating ball/3.5 turns lock-lock/10.36m Turning Circle |
| Brakes | vented discs front, solid discs rear |
| Wheels (Sport-Sahara-Opt) | 16X7 245/75R16 - 17X7.5 255/75R17 – 18X7.5 255/70R18 |
| Suspension (Front) | Dana 30 axle, leading arms, Panhard bar, coil springs, anti-roll bar, gas-charged shock absorbers |
| Suspension (Rear) | Dana 44 axle, trailing arms, Panhard bar, coil springs, high-pressure gas-charged shock absorbers |
| Max Towing Weight | 1,000kg | 2,200kg | 1,000kg |

WRANGLER